## Slide 1
Today Week 6: + feedback w/ Op Amps; FET Switches; Schmidt; S/H: H&H L10&11 Mon Mar 2
FOCUS on required Labs: 10-1, 2, 3 or 4, 7;
A. 11-1a), 11-1 B., 2, 3, 5;
Skim pp. 207-266: Use IRF 520 (vs 510) & rotate “spade” pins along axis by 90°.
Supply all pins of DG403 analog switch!!! see p259
OP-AMP as amplifier: a reprise typical voltage gain > 10,000, with biasing done for you = an impedance matcher: >>MΩ looking in input, <1Ω into output (Thevenin) gains determined by 2 external resistors. dc operating “sweet” spot done for you. ± 15v rails, with both op amp inputs “virtually” sitting at ground no Cinput or Coutput blocking of DC bias needed constant gain up to HF, temperature independent, highly linear output dynamic range (compliance)...symmetric saturation at rails distortion only when approaching slew rate...e.g. ~5 v/μsec, ~MHz Input dynamic range limited by enormous gain 2 Golden “ideal rules”: input voltage diff = 0 v, input current = 0 ma each has its limitations 2 classic configurations: inverting & non-inverting modify in innumerable ways with non-linear external “hair”
Iff you have negative feedback!
Today we explore +POSITIVE+ feedback
Before you leave each day, please be sure to stop me & show me what you’ve achieved!

## Slide 2
All pins must be tied down for it to work right!!! (except manufacture’s test, 2 & 7)

## Slide 3
FET’s: 2 flavors
JFET pnp, npn (pn) Junction FET, not used much these days
MOSFET Metal-Oxide-Semiconductor FET, thousands in every digital chip cf. 2N5485
p or n-type Si to form a conductive channel between source & drain on “substrate”
doped with B or Ph
heated in H2O vapor to form thin SiO2 insulator on surface
Al evaporated and deposited to form metal “gate”
run in enhancement mode: + gate attracts electron carriers in channel
- gate attracts “hole” carriers
a controllable current source, a 0Ω resistance switch with hi Zin
an analog switch for current traveling in either direction, S to D, or D to S ...not a pn junction, which has directionality
10k electrons on gate can switch 1 amp!
CMOS Complementary...p-channel and n-channels on same chip allow push-pull
digital computer logic, +5v = “on”, 0v = “off”, switches analog signals up to ± 15v rails
MOSFET natural figure of merit:
transconductance (gm) = ΔIout / ΔVin in micro-mho (mho = ohm-1 = 1/ohm, Ω upside down)
(used also for pentodes, the 5 element vacuum tube equivalent) pix p157
MOSFET Defects and Limitations:
charge injection = switching “on” or “off”, ~60 pC of charge spit out to drain (Coulombs)
feedthrough = dB of signal on gate that gets through to the drain due to stray (10pF)
Ron = non-zero Drain to Source resistance RDS when turned on...ideally 0Ω (~25Ω)
rf limitations: stray capacitance, at input: CGD & CGS & at output: CDG & CDS pixs p265

## Slide 6
SCHMITT TRIGGER and SAMPLE & HOLD...the 2 most important analog chips
OP AMP INNARDS
diff amps, current mirrors, push pull emitter followers pix p232
often with open-collector outputs...you select it externally with pull-up resistor
SCHMITT TRIGGER schematic p235
threshold to go “on” is higher than to go “off” = hysteresis
i.e. a discriminator LF311
= fast op amp with positive feedback 2 threshold diagram
SAMPLE & HOLD
samples a voltage, stores it, let’s it be digitized
¼ pc least count...4x stray capacitance + charge injection
S&H natural figures of merit:
acquisition time...how long to charge up sampling capacitor?
determines S&H speed (~msec)
droop rate...how fast does the charge on the capacitor leak off?
FET Defects and Limitations
charge injection = each time switch on or off, ~60pC of charge spit out to drain (Coulombs)
LEDs...Si, GaAs, GaInPh

## Slide 7
Mon, Mar 16, “must” skim H&H 281-341, focus on L13 & 14 & your Arduino: Digital Electronics: gates, binary logic with NANDs, Flip Flops…logic probes.
During Spring Break...
Prepare for Labs 13-1, 2, 4, 5, but no TTL; Labs 14-1, 2, 5-b
Take your Arduino microprocessor & cable home: you must bring your laptop with Arduino to lab.
Read Eric Hazen’s page for the minimal C you must know:
https://docs.google.com/document/d/1dNcLgDqVa4kXvEaW8MCvMPSsF3m3jEKtGxN8k60e8-o/edit
Follow Dan Gastler’s “Crash Course in C” lecture slides:
https://docs.google.com/presentation/d/18sV6cQqeDFwiH5KBWFixevLTHqkzHcVgzM-WMMHFghs/edit?usp=sharing
Download Arduino software to your laptop; do the “blink” tutorial at
http://arduino.cc/en/Tutorial/Foundations
Prepare for 45 min analog written exam (it’ll be easy) during that session, at 10:10
(11am if a class conflict at that time. )